PCB Exposure Unit
State Machine Description
v1.0
Dec 27 2017

# State Descriptions
State	On Entry	In State	To Exit
RESET	Load exposure time from EEPROM / Clear all lamps	n/a	Immediately after completing entry → READY
READY	Clear lamps & light READY	Display remaining time on 4-dig LED / Flash colon every ½ second	Start/Stop Button → RUN / Encoder Button → TIME-SET
RUN	Clear lamps and light RUN	If time remaining > 0, then after 1000ms, subtract 1 second / Display remaining time on 4-dig LED	Time <= 0 → FINISHED-BUZZER / Start/Stop Button → PAUSE
PAUSE	Clear lamps and light PAUSE	Display remaining time on 4-dig LED	Start/Stop Button → RUN / Reset Button → RESET
FINISHED-BUZZER	Clear lamps and light FINISH	Display 00:00 on 4-dig LED / Flash display every 0.25 seconds	Reset Button → RESET / After 5 seconds → FINISHED
FINISHED		Continue flashing display	Reset Button → RESET / Encoder Button → TIME-SET
TIME-SET	Load exposure time from EEPROM / Clear lamps and light TIME-SET	Display exposure time on 4-dig LED / Adjust up/down with encoder	Encoder Button → TIME-SAVE / Reset Button → RESET
TIME-SAVE	Store new time in EEPROM		Immediately → TBB-SET
TBB-SET	Load TBB Byte / Clear lamps & light TOP if T bit set / Light BOT if B bit set	Cycle T > Bot > Both with encoder / Clear lamps & set TOP and BOT per current setting	Encoder Button → TBB-SET / Reset Button → RESET
TBB-SAVE	Store TBB byte in EEPROM		Immediately → RESET

# Internal Variables
## State Management
- Current State (enum)
- Previous State (enum)
- Time In Current State (unsigned long)
- Display Lamp (byte) (see breakout, below)
## Run Timer related
- Configured Exposure Time (unsigned long)
- Remaining Run Time (unsigned long)
## Flashing and Beeping
- Display On Off State (bit)
- Last Display State Change (unsigned long)
- Flash Duration (int)
- Beep On Off State (bit)
- Last Beep State Change (unsigned long)
## Display Lamp Byte
- Bit0 – Ready
- Bit1 – Running
- Bit2 – Paused
- Bit3 – Finished
- Bit4 – Time Set
- Bit5 – TBB Set
- Bit6 – Top Panel
- Bit7 – Bottom Panel